PRESS RELEASE DL024

HEAT RESISTANT SEALS COVER SIX YEARS

PRODUCTION IN KEY THERMO FORMING PROCESS

Dupont™ Kalrez® Spectrum™ 6375 O-ring seals, which were fitted into thermo forming moulds producing components utilised in industrial process automation, have operated for six years at production steam temperatures up to 165°C without failure. This period of uninterrupted production has been calculated to represent a cost saving of nearly 140K Euro over the manufacturing period 2005-2010.

These cost savings result from reductions in down-time, with increased production reliability of the 14 large thermo forming moulds which represent the manufacturers’ key compression moulding process.

Other contributory factors in the cost savings include the elimination of O-ring replacement costs or the two days of downtime associated with the previous sealing product replacements. Very high maintenance costs were also incurred during the necessary cooling down and reheating periods required for seal replacements, together with additional stress loadings on production and maintenance personnel in the event of unexpected leaks.

Continued ……

Prior to the fitment of the Dupont™ Kalrez® Spectrum™ 6375 seals, the moulding manufacturer needed to replace the original FKM O-rings roughly every six months. The effect of hot steam on these products generated embrittlement, causing surface cracking, and a reduction in tensile strength leading to significant loss of sealing force and eventual leakages. Since replacement, the Mean Time Between Repair (MTBR) period has been increased by a factor of five, leading to increased yields, time saving and reduced maintenance. Even after five years operation, the Dupont™ seals remained leak-free and in good condition, and were only replaced during routine inspection as a precautionary measure.

The official Dupont™ licensee company Dichtomatik Ltd, can supply the range of high performance Kalrez® Spectrum™ products as well as full technical advice and support for customers. Kalrez® Spectrum™ 6375 perfluoroelastomer sealing products are designed to provide outstanding performance for operation over the widest range of chemicals and temperatures. This includes acids, bases, amines, steam, ethylene oxide and many other aggressive chemicals, as well as mixed streams. A continuous upper service temperature of 275°C (525°F) can be accommodated, which is approximately 100° higher than other sealing products claiming such broad chemical resistance. The high temperature stability translates to increased chemical resistance over all temperature ranges, especially where high temperature process excursions occur. High resistance to volume swell and compression set are also major benefits of the Kalrez® 6375 product range.

Further information is available from:

Dichtomatik Ltd, Donington House, Riverside Road, Pride Park, Derby  DE24 8HX

Telephone: 01332 524401                    	Fax: 01332 524425

e-mail: kalrez@dichtomatik.co.uk          www.dichtomatik-kalrez.co.uk

Continued ……

(approximately 440 words

including photographic annotation)

General Information

Supplier:					Dichtomatik Ltd

Press Release No:				DL024

Press or publishing inquiries to:	Steve Lloyd						The Coach House

Enterprise Marketing Services Ltd		1 Dunstall Road

Tel: +44 (0) 1283 713185				Barton under Needwood

Fax: +44 (0) 1283 716172				Burton on Trent			e-mail: info@enterprise-marketing.co.uk 	DE13 8AX

United Kingdom

Reader response inquiries to:		Mr D Cook of Dichtomatik Ltd

Downloads:				The press release text (MS Word and PDF format) and all images are

available for download at:

www.enterprise-marketing.co.uk/dl/dl024.html

Our Reference:				DL024/03/12

Heat resistant Dupont™ Kalrez® Spectrum™ 6375 O-ring seals, available from Dichtomatik Ltd, providing cost savings when utilised in industrial process automation.

Download high resolution 300dpi image

Download low resolution 72dpi image

END