PRESS RELEASE HLI34

NEW DRYERS FROM HI-LINE DESIGNED

FOR HIGH PERFORMANCE & LONG LIFE

A new range of point-of-use adsorption dryers called the Atacama range has been introduced by Hi-line Industries Ltd, the compressed air specialists. These new products replace their previous Hi-Zorb range, and have positively driven valves fitted throughout rather than the less reliable shuttle valves previously utilised. Good performance combined with high reliability has been achieved following the elimination of valve failure, leading to extended periods between routine services. The Atacama products, which are fitted as standard with both pre and post filtration facilities, provide dry air at a dewpoint of -40°C. Lower dewpoint models down to -70°C can also be supplied. They are suitable for applications in the medical, dental, food processing and packaging industries as well as powder coating, printing, laser technology, plasma cutting, pneumatic control and general manufacturing.

Well proven extruded aluminium technology is utilised for the twin desiccant filled towers comprising each dryer, each tower being sealed with aluminium valve blocks at the top. Incoming air is being dried as it passes through one desiccant bed while the adjoining dryer chamber is automatically being regenerated using the PSA (Pressure Swing Adsorption) principle. While operating, a small amount of the dried compressed air is used to regenerate the adjacent saturated desiccant bed. This is achieved by the expansion of the introduced air from line pressure to atmospheric pressure, so removing entrapped moisture within the desiccant and thus regenerating the dryer ready for the next change-over cycle. This change-over is instigated automatically, controlled by a digital controller.

Continued ……

This energy-saving system can be further upgraded where required by the introduction of a dewpoint hydrometer probe to provide automatic full dewpoint control. A dewpoint LED display is incorporated in the top right hand corner of the control panel. This smart controller feature can also be retro-fitted to all makes of dryer as an energy saving feature.

A total of 8 of these small, compact dryer models are available off-the-shelf for next day delivery. These cover air flow rates from 5 up to 100cfm, operating at a pressure range of 4 – 16 bar from a standard 240Vac supply.

Further information is available from: Hi-line Industries Ltd,

5 Crown Industrial Estate, Oxford Street, Burton on Trent, Staffordshire DE14 3PG

Telephone: 01283 533377                    		Fax: 01283 533367

E-mail: enquiries@hilineindustries.com		www.hilineindustries.com

(approximately 400 words

including photographic annotation)

General Information

Supplier:					Hi-line Industries Ltd

Press Release No:				HLI34

Press or publishing inquiries to:	Steve Lloyd

Enterprise Marketing Services Ltd

The Coach House, 1 Dunstall Road, Barton under Needwood,

Burton on Trent, Staffordshire, DE13 8AX, UK

Tel: +44 (0) 1283 713185

Fax: +44 (0) 1283 716172

E-mail: info@enterprise-marketing.co.uk

Reader response inquiries to:		Mr Steven D Smith
Sales & Marketing Director of Hi-line Industries Ltd

Downloads:				The press release text (MS Word and PDF format) and image are

available for download at:

www.enterprise-marketing.co.uk/hli/hli34.html

Our Reference:				HLI34/06/14/V1

Continued ……

One of the new Atacama range of adsorption dryers from Hi-line Industries Ltd, incorporating positively driven valves for maximum reliability and performance.

Download high resolution 300dpi image

Download low resolution 72dpi image

END