PRESS RELEASE HLI39

HI-LINE ‘BLUE-BAG’ TECHNOLOGY SETS INDUSTRY STANDARDS

A new concept in the treatment of compressor condensate discharge has been introduced by the air handling specialists Hi-line Industries Ltd. Their latest ConSEP products provide a 10% higher volumetric capacity than their previous Gen 2 range, enabling the utilisation of greater oleophilic as well as superior activated carbon filtration media. The increased service life provided by these products is backed-up with a lifetime warranty against leaks or malfunction provided by this established midlands manufacturer.

The ConSEP range exceeds all relevant UK and European consent levels, and is compatible with all current condensate drains as well as many types of oils. By eliminating moving parts, together with both static water and oil containers, the larger and stronger ConSEP ensures a simple, reliable and friendly environmental solution for the economical treatment of compressor condensate. The whole process is both easy and clean to use, ensuring a low carbon footprint with the provision of a 6 – 12 month service period between sediment collections and ‘blue-bag’ replacements.

Four models are available in the ConSEP condensate cleaner range, covering flow capacities of 100/300/750 and 1500 cfm respectively. The condensate, comprising residual air, water, oil and other process contaminants is fed into a diffusing lid on the individual ConSEP products. Where the condensate air content is de-pressurised and the discharge contents subject to primary filtration. The next stage of the process is an oleophilic filter chamber to collect entrained oil, followed by a separator body of activated carbon to filter out and remove any compression process contaminants and debris.

Continued ……

Clean water is collected at the bottom of the ConSEP vessel, with a water drain and test point also provided. Midpoint connectors are also provided to facilitate a multiple or modular grouping of up to five vessels to handle even large condensate output flows.

As an added incentive, a free ConSEP condensate cleaner will be provided with every Tundra Refrigerant Air Dryer ordered from Hi-line Industries Ltd during March 2015.

Further information is available from: Hi-line Industries Ltd,

5 Crown Industrial Estate, Oxford Street, Burton on Trent, Staffordshire  DE14 3PG

Telephone: 01283 533377                    		Fax: 01283 533367

e-mail: enquiries@hilineindustries.com		www.hilineindustries.com

(approximately 400 words

including photographic annotations)

General Information

Supplier:					Hi-line Industries Ltd

Press Release No:				HLI39

Press or publishing inquiries to:	Steve Lloyd

Enterprise Marketing Services Ltd

The Coach House, 1 Dunstall Road, Barton under Needwood,

Burton on Trent, Staffordshire, DE13 8AX, UK

Tel: +44 (0) 1283 713185

Fax: +44 (0) 1283 716172

E-mail: info@enterprise-marketing.co.uk

Reader response inquiries to:		Mr Steven D Smith
Sales & Marketing Director of Hi-line Industries Ltd

Downloads:				The press release text (MS Word and PDF format) and images are

available for download at:

www.enterprise-marketing.co.uk/hli/hli39.html

Our Reference:				HLI39/15/02/V2

Continued ……

The new ConSEP range of oil/water separators from Hi-line Industries for handling compressor condensate utilising the latest ‘blue-bag’ technology.

Download high resolution 300dpi image

Download low resolution 72dpi image

A new ConSEP 300 from Hi-line Industries Ltd, which can accommodate a full 300 cfm flow of compressor condensate discharge.

Download high resolution 300dpi image

Download low resolution 72dpi image

END